## Slide 1
🚜 ROBOTRAC R&D ENGINEERING SPECIFICATION
Autonomous Agricultural Tractor Platform
Technical Architecture, Drive-by-Wire Electro-Hydraulics, Dual-Domain Compute, Non-Linear Motion Control & ISO 18497 / ISO 25119 Compliance
Chief Technology Officer & Principal AI Robotics Engineer | October 2026

## Slide 2
SECTION 01 · AGRONOMIC CONTEXT
The Agricultural Robotics Challenge
REALITY CHECK
⚠️ Why Passenger AV Stacks Fail in Agriculture
• Terramechanics & Slip: Loose soil invalidates bicycle kinematics; slip reaches 15%–35%.
• Severe Environmental Blinding: Dust clouds and plant chaff coat optical sensors in 20 min.
• High-Mast Antenna Roll: Antenna at 2.8m causes up to 29.2 cm lateral error on 6° slopes.
• Dynamic Implement Drag: Asymmetric tillage forces (5–40 kN) generate violent yaw perturbations.
🎯 Robotrac Engineering Strategy
• Dual-Domain Compute: Hard Real-Time safety MCU for 100 Hz steering, separate from Linux.
• NMPC with Soil Slip: Active Pacejka tire-soil friction models compensate for side-slopes.
• Multi-Modal Radar Fusion: 77 GHz radar Doppler penetration validates obstacles in dust.
• Sub-Scale Electric Mule: Validate RTK and wireless E-stop at low risk before diesel tractors.

## Slide 3
SECTION 02 · SYSTEM ARCHITECTURE
Dual-Domain Compute Topology
ADR-002 APPROVED
🖥️ Domain 1: Soft Real-Time (NVIDIA Jetson)
• Hardware: NVIDIA Jetson AGX Orin Industrial (275 TOPS, -40°C to +85°C).
• OS & Middleware: Ubuntu Linux (PREEMPT_RT) + ROS 2 (CycloneDDS / Iceoryx).
• Perception: Optical NIR row segmentation (BiSeNet-V2 @ 30 FPS) + radar clutter filter.
• State Estimation: 15-state ES-EKF fusing dual RTK + tactical IMU @ 20 Hz.
• Planning: Fields2Cover coverage swaths, Ω-turns & acados NMPC solver (20 Hz).
🛡️ Domain 2: Hard Real-Time (Safety Controller)
• Hardware: TTControl TTC 580 / IFM CR711S (Dual-core lockstep MCU).
• Deterministic Loop: 100 Hz cycle (10.0 ms ± 0.1 ms jitter) running certified C/RTOS.
• Steering Actuation: Dual Hall WAS reading + Danfoss OSPE electro-hydraulic valve PWM.
• Fail-Safe Stopping: Spring-Applied Pressure-Released (SAPR) brake dump (< 150 ms).
• ISO 18497 E-Stop: Wireless RF remote heartbeat monitoring (< 500 ms automatic trip).

## Slide 4
SECTION 03 · VEHICLE CONTROL & DBW
Electro-Hydraulic Drive-by-Wire Subsystems
ISO 25119 AgPL d
Steering Actuation
• Danfoss OSPE / Eaton PVG 32 proportional valve with load-sensing priority.
• Zero mechanical backlash; direct cylinder hydraulic connection.
• Curtiss-Wright R300 dual Hall-effect WAS (IP69K sealed).
• Inverted analog plausibility check: V1 + V2 = 5.0V ± 0.1V.
Fail-Safe Braking
• Service Brake: Proportional pressure valve (0–120 bar) for smooth stops.
• Emergency Brake: Spring-Applied Pressure-Released (SAPR) cylinder.
• Fast Dump Valve: Vents hydraulic pressure to tank in < 150 ms on trip.
• Mechanical spring locks wheels independently of electrical bus.
Powertrain & Implement
• SAE J1939 Engine Control: Commands speed/torque limits via TSC1 message.
• ISOBUS Class 3 (ISO 11783): Automates 3-point hitch lift/lower at headlands.
• PTO Interlock: Disengages PTO automatically before tight Ω-turns.
• Electronic governor prevents engine stall under peak implement drag.

## Slide 5
SECTION 04 · STATE ESTIMATION
Dual-Antenna RTK & 3D Tilt Compensation
SUB-2.5 CM PASS
📡 Moving-Baseline Dual-Antenna RTK
• Hardware: Septentrio AsteRx-m3 Pro or Dual u-blox ZED-F9P on a 1.2m baseline.
• Static Yaw: Measures carrier-phase double-differences, guaranteeing sub-0.09° heading.
• Zero-Speed Reliability: True heading at 0 m/s; unaffected by wheel spin in mud.
• Magnetic Immunity: 100% immune to heavy tractor steel chassis distortion.
📐 Dynamic Terrain Roll / Pitch Compensation
• Tactical MEMS IMU: Xsens MTi-680G (< 2°/hr gyro bias stability) @ 200 Hz.
• Coordinate Transformation: Dynamic lever-arm tilt correction down to ground contact.
• Formula: Δx = h * sin(θ_roll) + l * cos(θ_pitch) eliminates mast sway.
• Ground Accuracy: Restricts lateral tilt error to ≤ 2.0 cm on uneven furrows.

## Slide 6
SECTION 05 · PERCEPTION ENGINEERING
Multi-Modal Sensor Fusion in Hostile Dust
ZERO FALSE STOPS
NIR HDR Cameras
• Leopard Imaging AR0820 GMSL2 (> 120 dB HDR, Global Shutter).
• NIR 850 nm Filter: Enhances crop chlorophyll reflectance vs dry soil.
• Pneumatic Air-Blast: 6-bar compressed air purge cleans lens dust every 5 min.
77 GHz mmWave Radar
• Continental ARS 408-21 automotive radar.
• Dust Penetration: Millimeter waves (3.9 mm) pierce dense tilling dust plumes.
• Direct Doppler: Instantly measures radial velocity of approaching humans.
3D Solid-State LiDAR
• Livox Mid-360 (360° x 59° FOV, 905 nm).
• Canopy Profiling: 3D field boundary, ditch, and canopy density extraction.
• Clutter Removal: Ground plane segmentation filters out harmless tall grass.